## Slide 1
DESIGN PROJECT
Student Guide
Balloon-Powered Racers

## Slide 2
LEARNING OBJECTIVES
  Understand simple engineering and design concepts behind racing cars
  Explore real world applications of Newton’s laws of motion
  Learn new applications of basic CAD features
  Design with constraints by applying design intent to the project
  Begin your own design iteration, balancing engineering functionality and creativity
  Explore and understand the basics of additive manufacturing (3D printing)

## Slide 3
BACKGROUND

## Slide 4
HISTORY
This design was inspired by several iconic early racers, such as the Alfa Romeo 158, Cooper T43, and Lotus 49. These vehicles were among the most advanced of their time, featuring streamlined bodies, open cockpits, and exposed wheels—all trademarks of early Grand Prix racing. Their designs prioritized speed and mechanical simplicity, each new model rapidly innovating over the competition of the mid 20th Century. Despite a lack of advanced tools, these cars handled exceptionally well at high speeds, laying the groundwork for modern racecar aerodynamics and design. This project pays tribute to their timeless style and engineering spirit.
Alfa Romeo 158/159
Cooper T43
Lotus 49
”Alfa Romeo 159” by Lennart Coopmans CC BY-SA 2.5
”A Cooper T43 in Formula Two Form” by Pyrope CC BY-SA 3.0
”The 49C being demonstrated in 2005” by Softeis CC BY-SA 3.0

## Slide 5
NEWTON’S LAWS OF MOTION
Newton’s three laws of motion describe how forces affect the movement of objects:
INERTIA: A body in motion remains in motion, or a body in rest remains at rest, unless acted upon by an external force.
FORCE = MASS x ACCELERATION: Acceleration of an object is proportional to the force applied to it, and inversely related to its mass.
ACTION & REACTION: For every action, there is an equal and opposite reaction.
These principles help us understand how the balloon propels the racer forward and how design choices impact the racer’s performance.
1. Balloon releases air into
the mount as it deflates
2. The air is expelled out
of the rear of the racer
3. There is an equal and opposite
Reaction due to the air expelling from
the rear, propelling the car forward

## Slide 6
BALLOON RACER TERMINOLOGY
Spoiler
Cockpit
Balloon Mount
Exhaust
Axle Caps
Wheels
Main Body
Inner Rim

## Slide 7
DESIGN TERMINOLOGY
Design Intent– In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. An example of design intent is how you create and dimension a hole in a block. In product design terms, Design Intent is how a product should look, function and feel to the user.
Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
DFM/DFAM – Design for Manufacturing or Design For Additive Manufacturing. In this activity, it is important to consider the material and capabilities of the 3D printer in order to achieve a functional design with minimal waste.
Nesting – In manufacturing, nesting refers to laying out cutting patterns on raw material to minimizing waste during manufacturing processes, such as laser cutting. In 3D printing, it is the process of laying out parts to fit on the bed of the 3D printer to print several components at one time.

## Slide 8
PROJECT DESIGN INTENT
  3D Printed
  Propelled Forward by deflating balloon
  No Necessary Fasteners or Adhesives
Wheels rotate freely on each axis
Axle Caps are fastened using a simple snap fit
Air released by the balloon exits through exhaust opening
Air released by the balloon enters through top mount
Spoiler is attached with snap fit in back
(Can be removed/redesigned)
Axles are extruded directly from the body
Each Part has a flat surface that allows for simple 3D printing setup

## Slide 9
COMPONENT
DESIGN

## Slide 10
COMPONENTS – MAIN BODY & BALLOON MOUNT
DESIGN INTENT
Acts as the main frame, holding all of the racer components together.
Axles extend directly off the sides of the body, keeping the design simple and fully 3D printable.
Balloon mount begins at the top, curves through the interior, and exits at the rear, providing a clean and functional airflow path for propulsion.
Rear Spoiler Mount is a simple cut out from the rear.
DFAM
Designed with a fully flat bottom to print directly on the build plate.
Only minimal support material will be needed under the axles and exhaust.
NOTE: Dimensions are provided for reference only and are not required to meet Design Intent. Units are in millimeters.

## Slide 11
COMPONENTS – WHEELS
DESIGN INTENT
Rotates freely on the axles while keeping the car stable and moving straight.
Diameter must be large enough to keep the racer from scraping the ground.
DFAM
Uses Flat-Pack Design, no support material necessary.
Components can be nested to print several at one time.

## Slide 12
COMPONENTS – AXLE CAPS
DESIGN INTENT
Snap-fits onto the end of the axle to secure the wheel while still allowing for easy removal.
DFAM
Uses Flat-Pack Design, no support material necessary.
Components can be nested to print several at one time.

## Slide 13
COMPONENTS – SPOILER
DESIGN INTENT
Snap-fit into the rear mount cutout for easy removal and redesigning.
Prevents the balloon from tipping backward
DFAM
Orient the part so the flat component is on the build plate.
Only minimal support material will be needed under the connector.
DESIGN CHALLENGE:
Use your CAD knowledge to design your own spoiler—get creative!

## Slide 14
3D PRINTING

## Slide 15
3D PRINTING – Nesting
Nest your parts to print many at one time—Every part necessary to assemble one car can be printed together on most printer beds.

## Slide 16
3D PRINTING – Standard Orientation
Orient the parts to minimize the use of support material by placing each one on their main flat face. Be sure to include supports for overhanging geometries.
When prototyping or printing with classmates, consider printing multiple parts at the same time.

## Slide 17
PROJECT TASKS
  Create the following racer components in CAD:
    Main body
    Wheels
    Axle Caps
    Spoiler
  Create an assembly of the car in CAD.
  Print the physical components on a 3D printer.
  Assemble the Balloon-Powered Racer.
  Race against other students in a drag racing style competition.
  Iterate on the design—Experiment in CAD or utilize external household items enhance the model.

## Slide 18
CLASS DISCUSSION
Questions:
Which of Newton’s Laws best explains how the car moves forward when powered by the balloon?
How does the spinning (rotational) motion of the wheels translate into the car’s forward (lateral) motion?
Questions:
How could changing the design or location of different features affect performance? Which aspects can we change to increase speed, endurance, or stability?
  Should we move the balloon mount to the middle?
  What happens if we widen the exhaust tube?
  What if the front was longer or heavier?
Consider the motion of the racer.
Think about how the components are designed and assembled.

## Slide 19
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 20
LOREM IPSUM
  XXX

## Slide 21
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX

## Slide 22
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum