## Slide 1
DESIGN PROJECT
Student Guide
FLYING GLIDER

## Slide 2
LEARNING OBJECTIVES
Implement design intent when in CAD
Utilize assembly features to visualize the of center of mass
Understand basics of laser cutting procedures
Perform analysis on how the glider flies

## Slide 3
BACKGROUND

## Slide 4
TIMELINE
These first flyers were invented in China. The largest of them could lift a person off of the ground!
Sir George Cayley first formalized the fundamental principles of flight. He used this knowledge to create the first glider that carried a person.
Supersonic jets were mainly developed for military purposes, but a few were developed for commercial purposes. The Concorde jet could fly from New York to London in only 3 hours!
These used a flame to heat a large balloon of air and were able to carry a few people at a time.
The first engine-powered and piloted aircraft took flight. The third prototype went on a 40 minute journey!
Fusing computers with flight has enabled for robust autopilot and control systems for airplanes. Modern airplanes are built for safety, efficiency, and passenger capacity.
Flying Kites: ~500BCE
First Glider: 1853
Supersonic Jets: ~1950s
Hot air balloons: ~1780s
Wright Flyer: 1903
Modern airplanes: ~1980s
These expanded on the concept of the hot air balloon, but were much larger. Some were able to carry over 40 people.
Airships: ~1880s

## Slide 5
ENGINEERING DEFINTIONS
Center of mass:
The spot on an object where its weight is evenly balanced.
If you were to try balancing an object on your finger, the center of mass is where it would be perfectly balanced.
Design intent:
The purpose behind how something is designed
Design for manufacturing:
The design intent for easy, cost-effective, and environmentally friendly production
Flat pack design:
Design for a product to be packed and shipped in a flat box.
Tolerance:
Additional space in holes for parts to fit together easier.

## Slide 6
WING
FUSELAGE
STABILIZER
BALLAST PIECES
FLYING GLIDER TERMINOLOGY

## Slide 7
ABOUT THE FLYING GLIDER
Fuselage:
In real aircraft it provides space for cargo, people, and fuel during flight.
Designed to be strong and light to securely hold all of the aircraft together.
Wing:
Creates lift, keeping the plane soaring through the air and from falling to the ground
The small upward tilt generates lift by pushing the air down, keeping the glider up
Stabilizer:
This horizontal stabilizer keeps the glider stable in flight
Prevents small winds or speed changes from knocking the aircraft to the ground
Ballasts:
These ballasts control the plane’s center of mass, simulating a pilot, cargo, or fuel
These are designed to bring the center of mass towards the front of the plane

## Slide 8
COMPONENT DESIGN

## Slide 9
WING
Design for Manufacturing:
Make the widest part of the wing where it slots into the fuselage.
Design Tip:
Add large fillets to the front corner of the wings for the air to smoothly travel over it.

## Slide 10
STABILIZER
Design for Manufacturing:
Make the stabilizer widest where it slots into the body.
Design Tip:
Make the horizontal stabilizer about 1/5th of the size of the main wing.

## Slide 11
FUSELAGE
Design for Manufacturing:
Cutouts should be the exact dimension of the wing and stabilizer with no tolerance.
Design Tip:
Make sure there’s enough material where the glider might break, like around the wing or on the nose.

## Slide 12
BALLASTS (4)
Design for Manufacturing:
Create the ballasts with a large face so they can be securely glued to the fuselage.
Design Tip:
Make successive ballasts smaller as they stick out from the fuselage.

## Slide 13
LASER CUTTING
  After the model is created in CAD, export the faces of each piece as a DXF file, a 2D drawing file.
  When laser cutting, follow the machine’s safety procedures and your shop safety protocols
  Nest the cuts together to minimize material waste, as shown below.

## Slide 14
MATERIAL CHOICE
  The material used for this project is [YOUR MATERIAL HERE]
  Material properties:
    Thickness: [YOUR MATERIAL THICKNESS HERE]
    Density: [OPTIONAL – YOUR MATERIAL DENSITY HERE]
    Origin: [OPTIONAL – WHERE YOUR MATERIAL COMES FROM]

## Slide 15
CLASS DISCUSSION QUESTIONS
This glider’s center of mass is balanced under the wing of the plane for a smooth flight. What would happen if it were nose heavy? Or if it was tail heavy?
Where else should the fuselage be strong, and where can it be thin? Consider forces from a crash landing or the air hitting the wing.
The further back the stabilizer is, the smaller it can be. What are some limits on how small you should make the stabilizer?
How does the shape of the wing influence how the glider can fly? Look into different types of planes and understand their wing types.

## Slide 16
PROJECT TASKS
Create all of the components of the glider.
  Wing
  Stabilizer
  Fuselage
  Ballasts
Create an assembly of the plane in CAD for design analysis
Manufacture the components from your design.
Assemble and test fly the glider.

## Slide 17
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 18
LOREM IPSUM
  XXX

## Slide 19
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum

## Slide 20
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX