## Slide 1
DESIGN PROJECT
Student Guide
KINETIC SCULPTURE

## Slide 2
LEARNING OBJECTIVES
  Understand how different mechanisms can convert rotational motion into linear motion.
  Identify and describe basic machine elements and their role in mechanical systems.
  Design with constraints by applying design intent to the project.
  Explore and understand additive manufacturing principles.
  Learn the basics of 3D printing.

## Slide 3
BACKGROUND

## Slide 4
HISTORY
Kinetic sculptures have existed for centuries, blending motion with storytelling and mechanical ingenuity. In ancient Greece, inventors like Hero of Alexandria built automata powered by falling weights, water, or air to create lifelike movement in temples and theaters.
During the Islamic Golden Age, engineer Al-Jazari designed intricate water-powered machines—musical automatons, mechanical peacocks, and programmable servants—that showcased early robotics and advanced control systems.
By the 18th and 19th centuries in Europe, automata flourished—delicate, hand-cranked figures like musicians and dancers used cams, gears, and linkages to animate complex scenes. In the 20th century, artists like Jean Tinguely brought kinetic sculpture into modern art, using motion itself as a creative medium.

## Slide 5
Stopper
Cam
Links
Pins
Yoke
Tail
Wings
Head
Stem
Flower
KINETIC SCULPTURE TERMINOLOGY
Crank
  The Scotch Yoke Mechanism is a mechanical linkage that converts rotary motion into linear motion (or vice versa) in a smooth, continuous way.
  In this design, a rotating crank drives a sliding yoke, which is connected to the wings via linkages.
  As the crank rotates, the yoke moves back and forth, translating the motion into symmetrical up-and-down flapping of the wings.

## Slide 6
DESIGN TERMINOLOGY
  Design Intent – In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. An example of design intent is how you create and dimension a hole in a block. In product design terms, Design Intent is how a product should look, function and feel to the user.
  Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
  DFM/DFAM – Design for Manufacturing or Design For Additive Manufacturing. In this activity, it is important to consider the material and capabilities of the 3D printer in order to achieve a functional design with minimal waste.
  Nesting – In manufacturing, nesting refers to laying out cutting patterns on raw material to minimizing waste during manufacturing processes, such as laser cutting. In 3D printing, it is the process of laying out parts to fit on the bed of the 3D printer to print several components at one time.

## Slide 7
PROJECT DESIGN INTENT
  3D Printed
  Snap together assembly, no adhesives
  Powered by crank
  Fully functional assembly

## Slide 8
COMPONENT
DESIGN

## Slide 9
BUTTERFLY LEFT WING
DESIGN INTENT
The left and right wings are symmetrical until the center connection is split.
The left wing features two axle mounts spaced to hold the right wing’s single mount between them, allowing both wings to rotate around a shared pivot.
DFAM
Minimal support is needed, link tab and Axle mount require small amounts due to their overhangs.
Orient so that the top flat face is on the build plate. Can still be nested to print several at one time with proper orientation.

## Slide 10
BUTTERFLY RIGHT WING
DESIGN INTENT
The right and left wing are symmetrical until the center connection is split.
A link tab (small tab with hole) connects the wing to a linkage.
An Axle mount (cylindrical feature with hole) connects to the Axle allowing the wing to rotate.
DFAM
Minimal support material is needed, but both the link tab and axel mounts require small amounts due to their overhangs.
Components are not flat-pack due to their 3D geometry, but can still be nested to print several at one time with orientation adjustments

## Slide 11
BUTTEFLY HEAD
DESIGN INTENT
Decorative and functional. Caps the end of the axle, meant to keep wings from slipping off when in motion.
Sized not to interfere with wings when moving.
Fillets to prevent snapping on thin small printed pieces.
DFAM
Minimal support material is needed, antennas and hole require small amounts due to their overhangs.
Component is not flat-pack due to their 3D geometry, but can still be nested to print several at one time with proper orientation.

## Slide 12
BUTTERFLY TAIL
DESIGN INTENT
Decorative and functional. Attaches to flower with mounting rod, secures Axle in position while wings are in motion.
Fillets to prevent snapping on thin small printed pieces.
DFAM
Minimal support material is needed, extended rod requires small amounts due to overhangs.
Component is not flat-pack due to its 3D geometry, but can still be nested to print several at one time with proper orientation.

## Slide 13
STEM
DESIGN INTENT
Decorative and functional. Rectangular cut through body serves as a linear motion guide for the yoke, preventing rotation with the cam.
Side mounted hole and shaft holder supports crank; extruded outward to stabilize it’s weight.
Wide-base for stability when force is applied.
Fillets added around leaves to reduce the risk of snapping
DFAM
Support material is needed, design features multiple overhangs. Use organic supports to minimize material usage and ease removal.

## Slide 14
FLOWER
DESIGN INTENT
Decorative and functional. Mounting sleeve secures tail rod to support wings at correct height.
Petal shapes are designed to avoid interference with flapping wings.
Snap-fits securely onto the top of the stem base while allowing for easy removal and interchangeability
DFAM
Component is not flat-pack due to its 3D geometry, but curved faces are designed to not need any supports.

## Slide 15
YOKE
DESIGN INTENT
Attaches two links to the driving mechanism.
Slot allows the pin to slide along its length as it follows a circular path causing the entire yoke to slide up and down in a linear path.
Keep thin to reduce weight of mechanism, add fillets and chamfers to reduce material.
DFAM
Uses Flat pack Design, no support materials necessary.
Component can be nested to print several at one time.

## Slide 16
LINK
DESIGN INTENT
Connects wings to yoke, allowing them to move up and down simultaneously when the yoke is actuated.
Add enough length to push wings above horizontal position, while preventing contact with the flower on the downward motion.
Keep thin to reduce weight of mechanism. Add fillets and chamfers to reduce material
DFAM
Uses Flat pack Design, no support materials necessary
Components can be nested to print several at one time

## Slide 17
CAM
DESIGN INTENT
Circular base with center hole for crank attachment.
Offset pin rotates in a circular path, driving yoke’s vertical motion.
Keep thin to reduce weight of mechanism. Add fillets to reduce material.
DFAM
Component is not flat-pack due to its 3D geometry, but with proper orientation supports are not needed.
Component can be nested to print several at one time

## Slide 18
PIN
DESIGN INTENT
Designed to securely connect wings to links, and links to yoke.
Wide head stops pin from passing completely through holes.
Pointed tip makes insertion easier and helps overcome minor 3D printing defects or misalignments
DFAM
Component is not flat-pack due to its 3D geometry, but with proper orientation supports are not needed.
Component can be nested to print several at one time

## Slide 19
STOPPER
DESIGN INTENT
Snap-fits onto cam’s pin to prevent yoke from slipping off during rotation.
Can be used as spacer when connecting link to wing’s link tab during assembly.
DFAM
Uses Flat pack Design, no support materials necessary.
Component can be nested to print several at one time.

## Slide 20
CRANK
DESIGN INTENT
Connects to cam and is manually rotated by the user to drive the mechanism.
Crank shape increases torque and improves leverage for easier rotation.
Snap-fits into cam, allowing them to rotate together.
DFAM
Minimal support material is needed, small amounts required due to overhangs caused by rounded shape.
Component is not flat-pack due to it’s 3D geometry, but can still be nested to print several at one time with orientation adjustments .

## Slide 21
3D PRINTING

## Slide 22
3D PRINTING – NESTING
  Components are nested.

## Slide 23
3D PRINTING – STANDARD ORIENTATION
  Support required, use organic support structures to maximize efficiency.

## Slide 24
PROJECT TASKS
Model the following kinetic sculpture components in CAD:
  Butterfly Wings
  Head and Tail
  Flower
  Stem
  Cam
  Link and yoke
  Pin and Stopper
  Crank
Create a working, moving assembly of the sculpture in CAD.
Print the physical components on a 3D printer.
Assemble the kinetic sculpture.

## Slide 25
CLASS DISCUSSION
Question:
Question:
What other power sources could be used to drive the same motion, and how might they change the design or interaction?
How could different linkages or cams affect the movements in your sculpture?
Consider that this sculpture is powered by hand cranking
Think about the mechanical motion created by the design

## Slide 26
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 27
LOREM IPSUM
  XXX

## Slide 28
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum

## Slide 29
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX