## Slide 1
DESIGN PROJECT
Student Guide
MARBLE RUN

## Slide 2
LEARNING OBJECTIVES
  Understand how gravity, potential, and kinetic energy are applied in designs involving motion.
  Explore the benefits and limitations of a modular design approach.
  Design with constraints by applying design intent to the project.
  Explore and understand manufacturing principles.
  Understand the basics of 3D printing.

## Slide 3
BACKGROUND

## Slide 4
ABBREVIATED HISTORY OF MARBLES
The earliest marbles date back to 2500 BCE and were found in the Indus Valley Civilization (modern day Pakistan and India).
A German glassblower invented marble scissors – a device used for easier production of glass marbles.
Marble runs gained popularity as an education tool and pastime – events were held worldwide.
Marbles have been discovered in the remains of ancient Mesopotamian, Egyptian, Greek, and Roman civilizations.
Glass marbles entered relatively inexpensive mass production, taking the world by storm.
Marble runs have appeal to everyone from young kids learning the basics of physics to engineers designing and fabricating complex marble runs!
2500 BCE
1846
1900s
2000 – 0 BCE
1870s
Today

## Slide 5
MARBLE RUNS
  Marble runs provide infinite design possibilities and range from simplified modular toys to complex motorized marble machines.
Areklodzpl, CC BY-SA 4.0 <https://creativecommons.org/licenses/by-sa/4.0>, via Wikimedia Commons

## Slide 6
DESIGN TERMINOLOGY
Modular Design – A design approach where a complex system is split into smaller parts, called modules, that can be easily connected. This approach increases a product’s adaptability and decreases waste during manufacturing because modules can be easily replaced and reconfigured.
Design Intent – In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. An example of design intent is how you create and dimension a hole in a block. In product design terms, Design Intent is how a product should look, function and feel to the user.
Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
DFM/DFAM – Design for Manufacturing or Design For Additive Manufacturing. In this activity, it is important to consider the material and capabilities of the 3D printer in order to achieve a functional design with minimal waste.
Nesting – In manufacturing, nesting refers to laying out cutting patterns on raw material to minimizing waste during manufacturing processes, such as laser cutting. In 3D printing, it is the process of laying out parts to fit on the bed of the 3D printer to print several components at one time.

## Slide 7
PROJECT DESIGN INTENT
All components are to be 3D Printed.
Minimize waste during prototyping by following a modular design approach.
All components should be compatible for easy re-arrangement.
Snap together assembly, no Fasteners or Adhesives.
NOTE: Dimensions are provided for reference only and are not required to meet Design Intent.

## Slide 8
Reconfigurable Design

## Slide 9
COMPONENT
DESIGN

## Slide 10
Marble Run Components
Sloped Track
Straight Track
Curved Track
Strut
Straight Connector
Curved Connector

## Slide 11
Marble Run Components
Support
Base Plate
Half Support
Start Basket
End Basket

## Slide 12
COMPONENTS – STRAIGHT TRACK
DESIGN INTENT
Guides forward marble movement.
Marble rolls smoothly and stays on track.
Can easily and securely attach and detach from connectors.
DFAM
Follows modular design principles for easier testing and to reduce material waste when reprinting.
Designed to minimize support material.
Components are nested to print several at one time.

## Slide 13
COMPONENTS – SLOPED TRACK
DESIGN INTENT
Guides vertical marble movement
Marble rolls smoothly and stays on track.
Can easily and securely attach and detach from connectors.
Has an overall height equal to two stacked supports.
DFAM
Follows modular design principles for easier testing and to reduce material waste when reprinting.
Designed to minimize support material.
Components are nested to print several at one time.

## Slide 14
COMPONENTS – CURVED TRACK
DESIGN INTENT
Guides marble turning.
Marble rolls smoothly and stays on track.
Can easily and securely attach and detach from connectors.
Is supported by struts to ensure stability.
DFAM
Follows modular design principles for easier testing and reducing material waste when reprinting.
Designed to minimize support material.
Components are nested to print several at one time.
Strut
Curved Track

## Slide 15
COMPONENTS – SUPPORT
DESIGN INTENT
Supports connector pieces.
Is able to stack on top of other supports.
Allows marbles to pass through with little to no resistance.
Has cutouts that match track profile.
DFAM
Follows modular design principles for easier testing and to reduce material waste when reprinting.
Designed to minimize support material.
Incorporates nesting to print several components at one time.

## Slide 16
COMPONENTS – HALF SUPPORT
DESIGN INTENT
Is able to stack on top of other supports.
Is half the height of typical support to increase arrangement options.
DFAM
Follows modular design principles for easier testing and to reduce material waste when reprinting.
Designed to minimize support material.
Incorporates nesting to print several components at one time.

## Slide 17
DESIGN INTENT
Provides a straight path between two tracks.
Matches track profile – marble stays on track.
Has secure connection points for tracks and struts.
Can stack on top of supports and allow supports to stack on top of it.
Same height as half supports for easy arrangement.
DFAM
Follows modular design principles for easier testing and reducing material waste when reprinting.
Designed to minimize support material.
Incorporates nesting to print several components at one time.
COMPONENTS - STRAIGHT CONNECTOR

## Slide 18
COMPONENTS – CURVED CONNECTOR
DESIGN INTENT
Provides curved path between two tracks.
Matches track profile – marble stays on track.
Has secure connection points for tracks and struts.
Can stack on top of supports and allow supports to stack on top of it.
Same height as half supports for easy arrangement.
DFAM
Follows modular design principles for easier testing and reducing material waste when reprinting.
Designed to minimize support material.
Incorporates nesting to print several components at one time.

## Slide 19
COMPONENTS – START AND END BASKETS
DESIGN INTENT
Provides controlled start/end of marble run.
Can stack on top of supports.
Has secure connection points for tracks and struts.
DFAM
Follows modular design principles for easier testing and reducing material waste when reprinting.
Designed to minimize support material.
Incorporates nesting to print several components at one time.

## Slide 20
COMPONENTS – BASE
DESIGN INTENT
Provides a wider base profile for added stability.
Allows supports, connectors, and baskets to stack on top of it.
Has holes for mounting (optional).
DFAM
Follows modular design principles for easier testing and to reduce material waste when reprinting.
Incorporates nesting to print several components at one time.

## Slide 21
Additional component Ideas

## Slide 22
3D PRINTING

## Slide 23
3D PRINTING – Tolerancing
These components are initially designed to be perfect fits in CAD, but 3D printers are not completely accurate.
Any component interacting with another will likely need to be adjusted based on printer resolution.
Holes and cuts are typically made larger than extrudes to account for these errors.

## Slide 24
3D PRINTING – Tolerancing
It is recommended that the bottom cut of each support, connector, and basket is made slightly wider than the top extrudes on connectors, supports, and bases.
The strut may need to be designed smaller than the slot on the connectors.
The hooks and connection points for tracks are designed with extra space, but may need additional tolerancing.

## Slide 25
3D PRINTING – Standard Orientation
Components are Nested.
Oriented for no support required.

## Slide 26
3D PRINTING – Standard Orientation
Components are Nested
Support required. Use organic/tree support structures to maximize efficiency.
Oriented to reduce support material and print time.

## Slide 27
3D PRINTING – Standard Orientation
Components are Nested.
Support required. Use organic/tree support structures to maximize efficiency.
Oriented to reduce support material and print time.

## Slide 28
PROJECT TASKS
Create the following marble run components in CAD:
  Straight Track
  Sloped Track
  Curved Track and Struts
  Support and Half Support
  Straight Connector
  Turn Connector
  Start and End Baskets
Create an assembly of the marble run in CAD.
Print the physical components on a 3D printer.
Assemble the marble run.

## Slide 29
CLASS DISCUSSION
Question:
Question:
What are the pros and cons of using a modular design approach for marble run designs?
How can different tracks be designed to retain the marble better?
Consider the various types of marble runs and the modular design process.
Think about the momentum of marbles as they traverse the tracks.

## Slide 30
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 31
LOREM IPSUM
  XXX

## Slide 32
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX

## Slide 33
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum